Eddie Gurnee
COSC 422
3/12/2014
Final Project Abstract

For my final project, I intend to enhance my Boe-bot (Severus), with the ability to react to an infrared signal. Once any of Severus's IR receivers receive an IR signal from a constructed IR transmitter (which shall act as a stun gun for Severus), a signal will be sent directly to the chip, pulsing with different data depending on the location location of the receiver on Severus. Given that incoming pulse, Severus shall turn away and flee from the source of the offending IR signal.

Requirements for the Project:
- 1 (or more) IR transmitters each constructed with:
  - 1 IR LED
  - 1 small breadboard
  - 1 battery pack
  - 1 push button
  - 1 x14 PIC chip (these can be less than 16 pins on these)
- 4 IR receivers (for each side of Severus)
- 4 x14 PIC chips (1 per receiver so it can send a custom signal with the location data to the main PIC chip)

The code for Severus should allow him to be absolutely autonomous, just wandering around exploring the area. The IR transmitters act as an interrupt to the main chip, telling it to turn away from the side that received the IR signal.

Looking forward, I have time and ability, there are a few extra features I would like to bestow upon Severus:
- When Severus is hit from the transmitter
  - he'll give a small squeal of pain (a la R2-D2)
  - he will speed up (in an attempt to escape the aggressors)
  - his health bar will decrease (a LED with bars)
  - after he has been hit three times, he turns off and dies, needing to get a restart signal to turn back on
Give Severus better collision detection, upgrade him with sonar to prevent him from walking into walls and obstacles

Extra features would require:
- 1 LED set to represent health
- 1 switch (per transmitter) to differentiate between sending an “On” command vs the “FIRE!” command
- 1 PING Ultrasonic Distance Sensor
- 1 Piezoelectric Speaker